## Slide 1
ACT-SYS-DT weekly update - 2

## Slide 2: Revision of Work Holder
Max. Size of Transducer : 30mm
Clamping Force - Springs / Elastics / ?

## Slide 3: Assembly of Updated Parts

## Slide 4: A Load of 50 N is applied at the Center
Result : the deflection at the center < 0.1mm. It is safe to use 5mm Al Plate

## Slide 5: Mounting the robot with Enclosure
Aluminium extrusion of 45mm are placed on the base plate which allows the entire assembly to be mounted on the 5mm Al plate using L clamps.

## Slide 6: Updated torque calculation
Torque calculation was done considering all the components including the minor ones.
The effect of inertial torque was also considered in the selection of motor.
τ total = τ load +τ inertia
= (859.08+1032.9)*2.5
= 4729.95 Nmm

## Slide 7: Derivation of Jacobian Matrix
Why Jacobian Matrix : This matrix relates the cartesian velocity (transducer holder velocity) to the Angular
velocity of the motors.
Jacobian Matrix is derieved from differentiating the position function.
(x -( l1 + l2cosθ-r) )² + y² + (z-l2sinθ)² = R²
(x +0.5( l1 + l2cosψ-r) )² + (y+0.866( l1 + l2cosψ-r) )² + (z-l2sinψ)² = R²
(x +0.5( l1 + l2cos∅-r) )² + (y-0.866( l1 + l2cos∅-r) )² + (z-l2sin∅)² = R²

## Slide 8: Differentiating Eqn 1 with time 2(x-(l1+l2cosθ -r ))(vx + l2sinθ(dθ/dt)) + (2yvy) + 2(z-l2sinθ)(vz - l2cosθ(dθ/dt)) = 0 Differentiating Eqn 2 with time (x+0.5(l1+l2cosψ -r ))(vx + l2sinψ(dψ/dt)) - 1.732(y+0.866( l1 + l2cosψ-r) )(vy+l2sinψ(dψ/dt)) + 2(z-l2sinψ)(vz - l2cosψ(dψ/dt)) = 0 Differentiating Eqn 3 with time (x+0.5(l1+l2cos∅ -r ))(vx + l2sin∅ (d∅/dt)) + 1.732(y-0.866( l1 + l2cos∅-r) )(vy+l2sin∅ (d∅/dt)) + 2(z-l2sin∅)(vz - l2cos∅ (d∅/dt)) = 0

## Slide 9: Simplified model for derivation of Jacobian matrix

## Slide 10: Simplified model for derivation of Jacobian matrix